Zach D'Agostino

Homework 1

Describe the difference between volatile and non-volatile memory.
    Indicate two types of memories which are volatile and two which are non-volatile.

Volatile memory can store and retrieve data quickly and is deleted when the unit is powered down. Memory is stored temporarily.
Examples: RAM (Random Access Memory) and Cache Memory

Non-volatile memory is slower to store and retrieve data but is not lost when unit is powered down. Memory is permanently stored.
Examples: ROM (Read Only Memory) and Flash Memory

Get the ATMega168 datasheet, go to the Register Summary section (about Section 35).
The list below includes SRAM Special Function Registers (SFR) or a bit within a SFR.
Identify the register name and SRAM address, and if it is a bit, find its bit position (bit0 to bit7).

  1. SREG – (0x5F) -AVR Status Register

  1. PORTB – (0x25) Port B Data Register

  1. EEDR – (0x40) EEPROM Data Register

  1. TCCR0B – (0x45) Timer/Counter Control Register B

  1. DDRC6 - (0x27) Bit 6 of the Port C Data Direction Register

  1. EEPE - (0x3F) Bit 1 of the EEPROM Control Register

Write the AVR assembly code that will set all the bits to 1 into the following SRAM addresses: 0x0000, 0x0001 and 0x0002.

ser r16
mov r0, r16
mov r1, r16
mov r2, r16

Write the AVR assembly code that will set all the bits to 1 into the following SRAM addresses: 0x0200, 0x0201 and 0x0202.

ser r16
sts 0x0200, r16
sts 0x0201, r16
sts 0x0202, r16